## Slide 1
Curve that is trajectory of a point M jointed to a moving circle kh(Sh, rh) that is rolling over a fixed circle kp(Sp, rp) (or line) is a cycloidal curve - cycloid. One branch of a cycloid is generated by one roll-off of circle kh over fixed circle (or line) kp, while circumference of the rolling circle kh is winded on the fixed circle kp. Thus the cycloidal movement is composed from two rotations about parallel axes passing through centres of the circles perpendicularly to the plane, in which both are located.
5.2 Cycloidal curves

## Slide 2
By different combinations of superposition of circles kh and kp , (or circle and line, which is regarded as circle with infinitely large radius), the following types of cycloids are obtained:
Epicycloid – moving circle kh is rolling by its outer circumference on the outer circumference of fixed circle kp.
Hypocycloid – moving circle kh is rolling by its outer circumference on the inner circumference of fixed circle kp (rh < rp).
Pericycloid – moving circle kh is rolling by its inner circumference on the outer circumference of fixed circle kp (rh > rp).
Pericycloidal movement is reversible to the epicycloidal movement,
therefore trajectories of these movements are the same curves.
4. Orthocycloid – moving circle kh is rolling on the fixed line kp.
Length of one branch of orthocycloid equals to the circumference of the moving circle.
5. Involute of a circle – moving line kh is rolling on a fixed circle kp.

## Slide 3
Distance d = MSh of moving point M from the centre Sh of moving circle kh determines type of cycloid:
If d  rh, then trajectory of point M movement is prolate cycloid.
If d = rh, then trajectory of point M movement is simple cycloid.
If d  rh, trajectory of point M movement is curtate cycloid.
Ratio of radii of fixed and moving circle, , determines number of cycloid branches generated by the motion of point M. Curve is closed if p is an integer.
prolate epicycloid simple hypocycloid curtate orthocycloid

## Slide 4
Epicycloid
curtate open prolate closed
,
,

## Slide 5
Epicycloid – rp : rh = 2 : 1
Nefroid prolate Nefroid simple

## Slide 6
Epicycloid – rp : rh = 1 : 1
Cardioid (simple) Limaçon of Pascal (prolate)

## Slide 7
Hypocycloid
curtate prolate
,
,

## Slide 8
Hypocycloid – rp : rh = 2 : 1
curtate – elliptic motion simple – line segment

## Slide 9
Steiner hypocycloid – rp : rh = 3 : 1
simple prolate

## Slide 10
Steiner hypocycloid curtate Asteroid (simple hypocycloid)
rp : rh = 3 : 1 rp : rh = 4 : 1

## Slide 11
Pericycloid ,
,
Limaçon of Pascal (curtate) prolate
rp : rh = 1 : 1

## Slide 12
Orthocycloid
simple prolate

## Slide 13
Involute of a circle
Simple Archimedean spiral – rp = d